- 产品简述

NT-EN1400是一款以太网到铜轴线转换设备。可成对使用或一对多使用。该设备可使用电话线、网线、双绞线或同轴线等各种常见线缆，实时传输。并具有优良的隔离，防雷抗干扰能力。在实际工程中，延长距离最远可达到1500米，最大通讯速率可以达到70Mbps，从而使工程无需重新布线，可以充分利用现有网络电缆。这样不仅实现了网络高清监控系统改造项目无需重新布线的愿望，进一步扩大了系统辐射范围，同时最大限度的降低了工程造价

NT-EN1400 is a device for Ethernet to coax featuring Coax to UTP connectivity. Can be used in pairs or a pair of much use

. It efficient transmission by common cable such as ADSL, UTP,or coax cable up to 1500meteres. With high performance in thunder prevention and anti-jamming. And in the practical project. its network communication rate can max.up to 70Mbps so that engineer need not relay fiber cable. Not only complement upgrade Network high-definition monitor and also further in expand scope and reduce project cost.

NT-EN1400-AT(AF)系列POE版本提供的１个POE供电端口，通过网线为基于POE技术给高清网络摄像机、无线AP、IP电话等设备供电，NT-EN1400有４个BNC接口可以做成汇聚点设备,也可以用其中的两个BNC接口组环.

NT-EN1400-AT(AF)POE series provide 1POE port can supply with network cable to HD camera、wireless AP、IP phone and others equipment. It can combine for 4 BNC port, also can be ringed with two of the BNC ports.

我司的EOC支持IEEE802.3af标准的15.4W功率输出,可选IEEE802.3at标准的25.5W功率输出.

EOC output 15.4 for IEEE802.3af, 25.5w for IEEE802.3at

我司的NT-EN1400支持POC供电（后端通过铜轴线给前端设备供电和IP摄像头供电）,默认本设备为Master端.

NT-EN1400 support POE supply(on the receiver can support POE to transmitter and IP camera by coax).its in the master

- 功能特点function feature

*  调制频段modulation frequency:２Mhz　-　２８Mhz

*  调制方式Modulation means：OFDM

*　加密方式Security mode：AES128-bit encryption

*　最大组网数Max. network：１个Master + 7个Slave

*  支持协议protocol：IEEE802.3/u　10Base-T、100Base-TX、　IEEE802.1Q VLAN、 IEEE802.3af/at

*  网口自适应直通线和交叉线，能兼容各种网卡，交换机，HUB等以太网设备

The port can auto-adapt to through line and cross spider, able compliant Ethernet equipment,such as network card,switch,HUB and so on.

*  支持最大1522Bytes数据包传输

Support Max.data package up to 152Bytes

*  支持线速转发和全双工流量控制/半双工背压模式

Support line-speed forwarding and full duplex flow control/half duplex back pressure

*  12V至56V DC宽电源输入

Wide rang DC input from 12V to 56V

*  -20到70℃操作温度满足各种复杂环境

In kingly complex condition, Operating temperature rang-20～70℃

*  支持以太网ESD保护和直流电源EFT保护

Support Ethernet ESD protection and direct-current EFT protection

*  支持单口POE供电可达15.4W /25.5

support single port for POE supply up to 15.4w/25.5

技术指标:

| 参数parameter | 规格specification |
| --- | --- |
| 设计等级design level | 商用级设计标准commercial standard |
| 接入方式conversation means | 10/100Mbps |
| 标准standard | IEEE802.3/u、10Base-T、100Base-TX、IEEE802.1Q VLAN、IEEE802.3af/at |
| 传输距离transmission distance | BNC线（SVY75-5）：1.5Km （TCP/IP最大70Mbps） 五类双绞线5 twist pair：100m |
| 端口 port | 1个RJ45口： 连接STP/UTP五类双绞线 ４个BNC口： Q9 |
| 流量控制flow control | 全双状态full duplex：流量控制flow control, 半双工状态half duplex：背压方式back pressure |
| 误码率BER | <10-9 |
| MTBF | 5万小时50000hours |
| LED指示灯LED indicator | PWR---电源灯power light, LAN---以太网连接/活动Ethernet connection/, Coax---铜轴线连接coax connection |
| 电源power | 电源输入范围input rang：12~56VDC |
| 功耗power consumption) | <6W（不提供POE供电时） |
| 储存湿度storage humidity(no condensation) | 5%~90%无凝结 |
| 工作湿度maintaining humidity(no condensation) | 5%~90%无凝结 |
| 工作温度maintaining temperature | -20~70℃ |
| 储存温度storage | -40~85℃ |
| 尺寸size | 台式：110mm×96mm×30mm （长×宽×高） |
| 重量weight |  |

| 技术认证technical certification |
| --- |
| EMI | FCC Part 15, CISPR (EN55022) class A |
| EMC | FCC,CE |
| EMS | EN61000-4-2 (ESD), Level 4 EN61000-4-3 (RS), Level 3 EN61000-4-4 (EFT), Level 4 EN61000-4-5 (Surge), Level 4 EN61000-4-6 (CS), Level 3 EN61000-4-8, Level 5 EN61000-4-11 |
| 震动vibration | IEC 60068-2-27 |
| 自由落体free fall | IEC 60068-2-32 |
| Vibration | IEC 60068-2-6 |
| 绿色环保green | RoHS，CRoHS，WEEE |

应用application solution

1.组环ring

２.级连cascade

３.汇聚combine

尺寸size

# Text boxes

EOC以太网视频同轴线传输器

NT-EN1400

EOC以太网视频同轴线传输器

NT-EN1400

# 工业级以太网光纤收发器系列

NT-IN311

# 工业级以太网光纤收发器系列

NT-IN311

EOC以太网视频同轴线传输器

NT-EN1400

EOC以太网视频同轴线传输器

NT-EN1400