### 概述

NC8124PGM 是一款16口全千兆三层网管交换机，最大支持12个千兆电口和4个千兆光口；12个千兆电口支持PoE+，符合IEEE802.3af/at标准，单口PoE功率可达30W。

NC8124PGM 支持三层网管，例如OSPF，RIP，QoS，VLAN，MSTP，多播，端口管理和PoE管理等；

NC8124PGM 具备较高的抗干扰能力，产品支持6KV防雷，8KV/15KV防静电，可以使用在多种环境中。

NC8124PGM 支持挂墙、桌面安装和Din-rail方式安装，工作可靠，坚固耐用，可使用在安防网络视频监控，网络工程等场合。

### 图片

### 特点

- 带12个10/100/1000M PoE下联电口，4个1000M上联光口；12个千兆电口支持PoE+，符合IEEE802.3af/at标准，单口PoE功率可达30W。

- 支持3层网管功能，例如OSPF，RIP，QoS，VLAN，MSTP，多播，端口管理和PoE管理等；

- 具备较高的抗干扰能力，产品支持6KV防雷，8KV/15KV防静电，可以使用在多种环境中；

- 支持工作温度 -40℃～75℃；

- 支持挂墙、桌面安装和Din-rail方式安装，工作可靠，坚固耐用，可使用在安防网络视频监控，网络工程等场合。

### 规格

| 项目 | 规格 |
| --- | --- |
| 电源 | 电源适配器供电，DC48~57V |
| 功耗 | 自身消耗<20W |
| 下联端口 | 电口1~12 10/100/1000Base-T PoE ports |
| 上联端口 | 光口 13~16 1000Base-X SFP |
| 传输介质和距离 | 使用 cat5e/6标准网线，最大100m |
| 网络标准 | IEEE802.3, IEEE802.3u, IEEE802.3z |
| 交换容量 | 32Gbps |
| 包转发率 | 23.8Mpps |
| 包数据缓存 | 4M bits |
| MAC 地址表 | 16K |
| 指示灯 | 电源：2 个红色; 上联 13~16光口：绿色LED指示Link/Act 下联1~12电口： RJ45 绿色LED指示 Link/Act，黄色LED指示PoE |
| 防护 | 浪涌： 6KV, 执行标准IEC61000-4-5 ESD： 8KV接触放电 15KV空气放电，执行标准IEC61000-4-2 |
| 工作温度 | -40℃~75℃ |
| 存储温度 | -40℃~85℃ |
| 湿度 | 0~95%（无凝结） |
| 尺寸（L×W×H） | 165 mm×115 mm×46mm |
| 外壳材质 | 金属 |
| 颜色 | 黑色 |
| 净重 | 530g |

软件：

| L2 Features | Port configuration | Auto-negotiation |
| --- | --- | --- |
|  |  | Flow Control |  |
|  |  | Port Mirror |
|  |  | Traffic statistics |
|  | Link Aggregation | Static link aggregation |
|  |  | LACP |
|  |  | Algorithm based on Source/Destination MAC |
|  |  | Algorithm based on Source/Destination IP |
|  |  | 8 groups |
|  |  | 8 ports per group |
|  | MAC Table | Aging Time |
|  |  | Static MAC address |
|  |  | Dynamic MAC address management |
|  | VLAN | 4K Active VLANs |
|  |  | 4K VID |
|  |  | 802.1Q Tag VLAN |
|  |  | Port VLAN |
|  |  | Protocol VLAN |
|  |  | MAC VLAN |
|  |  | Management VLAN |
|  |  | Voice VLAN |
|  |  | Q-in-Q |
|  |  | Private VLAN |
|  |  | GARP/GVRP |
|  | ACL | 64 ACLs |
|  |  | L2, L3 e L4 |
|  |  | Time-based ACL |
|  | Spanning tree | 802.1D Spanning Tree Protocol (STP) |
|  |  | 802.1w Rapid Spanning Tree Protocol (RSTP) |
|  |  | 802.1s Multiple Spanning Tree Protocol (MSTP) |
|  |  | Loop Guard |
|  |  | Root Guard |
|  |  | TC-BPDU Guard |
|  |  | BPDU Guard |
|  |  | BPDU Filter |
|  | Multicast | 256 groups |
|  |  | IGMP v1/v2/v3 |
|  |  | Fast Leave |
|  |  | Multicast VLAN |
|  |  | Static Multicast |
|  |  | Multicast Filter |
|  |  | IGMP Statistics |
|  |  | MLD Snooping |
|  | PoE management | Support total power consumption control |
|  |  | Support single port PoE ON/OFF |
|  |  | Support port output priority |
|  | QOS | 4 priority queues |
|  |  | CoS port-based |
|  |  | CoS 802.1p-based |
|  |  | CoS DSCP-based |
|  |  | Scheduling algorithms SP, WRR, SP+WRR |
|  |  | Storm Control (Broadcast, Multicast, Unknown Unicast) |
|  |  | Bandwidth control per port |
| Security Features | Port Security |
|  | MAC address filter |
|  | ARP Association (Manual, ARP scanning, DHCP snooping) up to 200 entries |
|  | ARP Protection |
|  | DoS (Denial of Service) |
|  | Classification of packages based on: End.MAC, IP End, TCP / UDP Ports, Protocol Type |
|  | 802.1x Autentication (port-based e MAC-based) |
|  | TACACS/TACACS+ Autentication |
|  | RADIUS Autentication |
|  | DHCP Filter |
|  | Guest VLAN |
|  | SSLv2/SSLv3/TLSv1 |
|  | SSHv1/SSHv2 |
|  | Restriction of WEB access based on: IP Address, And. MAC and Port |
|  | Port Isolation |
|  | Local User Name Password Authentication (2 levels) |
|  | Loopback detection |
| Management | SNMP v1/v2c/v3 |
|  | RMON 4 grupos |
|  | WEB (HTTP/HTTPS) |
|  | CLI (Telnet, Console, SSHv1/v2) |
|  | Firmware upgrade via console/web/TFTP |
|  | Configuration Backup/Reload |
|  | All possible configurations in the CLI must exist in the WEB interface |
|  | LLDP |
| Other Features | DHCP Relay |
|  | DHCP Client |
|  | DHCP Snooping |
|  | DHCP Option 82 |
|  | SNTP Client |
|  | BOOTP Client |
| Maintenance | Ping and Tracert |
|  | System log (Local and Remote) |
|  | Memory and CPU Monitoring |
| L3 Features | Static Routing |
|  | OSPFv2 |
|  | RIPv1/v2 |
|  | DHCP Server |
| IPV6 | IPv6 neighbor discovery (ND) |
|  | Path maximum transmission unit (MTU) discovery |
|  | Internet Control Message Protocol (ICMP) version 6 |
|  | TCPv6/UDPv6 |
|  | Ping6 |
|  | Tracert6 |
|  | Telnet(v6) |
|  | Http/Https |
|  | IPv6 TFTP |
|  | Static Routing |
|  | Interface IPV6 |

### 应用

### 面板图

### 结构图

### 订购信息

| 型号 | 描述 |
| --- | --- |
| NIE8124PGM | DC48-57V输入； 带12个千兆PoE电口，4个千兆光口； 带三层网管； 支持6KV防雷，8KV/15KV防静电； -40℃~75℃工作温度。 |