### 概述

NIE3244GM（4GS）是一款28口全千兆网管型交换机，最大支持24个千兆电口和4个千兆光口。

NIE3244GM（4GS）带2层网管，如QoS、VLAN、MSTP、多播和端口管理等。

NIE3244GM（4GS）具备较高的抗干扰能力，产品支持6KV防雷，6KV/8KV防静电，可以使用在多种环境中。

NIE3244GM（4GS）支持挂墙和桌面安装，工作可靠，坚固耐用，可使用在安防网络视频监控，网络工程等场合。

### 照片

### 特点

- 带24个10/100/1000M下联电口, 和4个1000M SFP光口；

- 带2层网管，如QoS、VLAN、MSTP、多播和端口管理。

- 具备较高的抗干扰能力，产品支持6KV防雷，6KV/8KV防静电，可以使用在多种环境中；

- 支持工作温度-40℃~75℃；

- 支持挂墙和桌面安装，工作可靠，坚固耐用，可使用在安防网络视频监控，网络工程等场合。

### 规格

| 项目 | 规格 |
| --- | --- |
| 电源 | 交流电源，AC100~240V，DC24-75V |
| 功耗 | 自身消耗<25W |
| 下联端口 | 电口1~24 10/100/1000 Base-TX RJ45 |
| 上联端口 | 光口 25~28 1000Base-X |
| 2层网管 | CLI:使用console端口(38400 8N1); Web:使用1-28个端口之一; 支持QoS、VLAN、MSTP、多播、端口管理等。 |
| 传输介质和距离 | 使用 cat5e/6标准网线，最大100m |
| 网络标准 | IEEE802.3, IEEE802.3u, IEEE802.3z |
| 交换容量 | 56Gbps |
| 包转发率 | 42Mpps |
| 包数据缓存 | 4M |
| MAC 地址表 | 16K |
| 指示灯 | 电源：1 个红色; 上联 25~28 光口：绿灯指示Link/Act, 下联1~24电口： RJ45 绿色LED指示 Link/Act |
| 防护 | 浪涌：6KV, 执行标准IEC61000-4-5 ESD：6KV接触放电 8KV空气放电，执行标准IEC61000-4-2 |
| 工作温度 | -40℃~75℃ |
| 存储温度 | -40℃~85℃ |
| 湿度 | 0~95%（无凝结） |
| 尺寸（L×W×H） | 442 mm×285 mm×22mm |
| 外壳材质 | 金属 |
| 颜色 | 黑色 |
| 净重 | 5kg |

软件：

| L2 Features | Port configuration | Auto-negotiation |
| --- | --- | --- |
|  |  | Flow Control |
|  |  | Port Mirror |
|  |  | Traffic statistics |
|  | Link Aggregation | Static link aggregation |
|  |  | LACP |
|  |  | Algorithm based on Source/Destination MAC |
|  |  | Algorithm based on Source/Destination IP |
|  |  | 8 groups |
|  |  | 8 ports per group |
|  | MAC Table | Aging Time |
|  |  | Static MAC address |
|  |  | Dynamic MAC address management |
|  | VLAN | 4K Active VLANs |
|  |  | 4K VID |
|  |  | 802.1Q Tag VLAN |
|  |  | Port VLAN |
|  |  | Protocol VLAN |
|  |  | MAC VLAN |
|  |  | Management VLAN |
|  |  | Voice VLAN |
|  |  | Q-in-Q |
|  |  | Private VLAN |
|  |  | GARP/GVRP |
|  | ACL | 64 ACLs |
|  |  | L2, L3 e L4 |
|  |  | Time-based ACL |
|  | Spanning tree | 802.1D Spanning Tree Protocol (STP) |
|  |  | 802.1w Rapid Spanning Tree Protocol (RSTP) |
|  |  | 802.1s Multiple Spanning Tree Protocol (MSTP) |
|  |  | Loop Guard |
|  |  | Root Guard |
|  |  | TC-BPDU Guard |
|  |  | BPDU Guard |
|  |  | BPDU Filter |
|  | Multicast | 256 groups |
|  |  | IGMP v1/v2/v3 |
|  |  | Fast Leave |
|  |  | Multicast VLAN |
|  |  | Static Multicast |
|  |  | Multicast Filter |
|  |  | IGMP Statistics |
|  |  | MLD Snooping |
|  | QOS | 4 priority queues |
|  |  | CoS port-based |
|  |  | CoS 802.1p-based |
|  |  | CoS DSCP-based |
|  |  | Scheduling algorithms SP, WRR, SP+WRR |
|  |  | Storm Control (Broadcast, Multicast, Unknown Unicast) |
|  |  | Bandwidth control per port |
| Security Features | Port Security |
|  | MAC address filter |
|  | ARP Association (Manual, ARP scanning, DHCP snooping) up to 200 entries |
|  | ARP Protection |
|  | DoS (Denial of Service) |
|  | Classification of packages based on: End.MAC, IP End, TCP / UDP Ports, Protocol Type |
|  | 802.1x Autentication (port-based e MAC-based) |
|  | TACACS/TACACS+ Autentication |
|  | RADIUS Autentication |
|  | DHCP Filter |
|  | Guest VLAN |
|  | SSLv2/SSLv3/TLSv1 |
|  | SSHv1/SSHv2 |
|  | Restriction of WEB access based on: IP Address, And. MAC and Port |
|  | Port Isolation |
|  | Local User Name Password Authentication (2 levels) |
|  | Loopback detection |
| Management | SNMP v1/v2c/v3 |
|  | RMON 4 grupos |
|  | WEB (HTTP/HTTPS) |
|  | CLI (Telnet, Console, SSHv1/v2) |
|  | Firmware upgrade via console/web/TFTP |
|  | Configuration Backup/Reload |
|  | All possible configurations in the CLI must exist in the WEB interface |
|  | LLDP |
| Other Features | DHCP Relay |
|  | DHCP Client |
|  | DHCP Snooping |
|  | DHCP Option 82 |
|  | SNTP Client |
|  | BOOTP Client |
| Maintenance | Ping and Tracert |
|  | System log (Local and Remote) |
|  | Memory and CPU Monitoring |
| IPV6 | IPv6 neighbor discovery (ND) |
|  | Path maximum transmission unit (MTU) discovery |
|  | Internet Control Message Protocol (ICMP) version 6 |
|  | TCPv6/UDPv6 |
|  | Ping6 |
|  | Tracert6 |
|  | Telnet(v6) |
|  | Http/Https |
|  | IPv6 TFTP |
|  | Static Routing |
|  | Interface IPV6 |

### 面板示意图

### 应用

### 结构图

### 订购信息

| 型号 | 描述 |
| --- | --- |
| NIE3244GM（4GS） | 带24个10/100/1000 下联电口, 和4个1000M SFP光口； 支持6KV防雷，6KV/8KV防静电，可以使用在各种恶劣环境中； 带两层网管功能。 |